## Slide 1: GE VENTILATOR FLUCTUATING DEMAND

## Slide 2: AGENDA
Executive Summary
Data Analysis
Value Stream Map Findings
Current & Future Challenges
Summary/Next Steps

## Slide 3: EXECUTIVE SUMMARY
Problem : Ventilator demand in surge, but
ventilator supply constant
Reason : Unexpected emergence of the
fatal COVID-19 pandemic
Solution : Identifying and addressing bottlenecks
in the production process

## Slide 4: DATA ANALYSIS
IQM and SD of Actual data :
8406.9 & 752.05
IQM and SD of Forecasted data :
766.9 & 148.6
Difference in the two averages :
7639.9

## Slide 5: VALUE STREAM MAP FINDINGS
1
Bottlenecks are similar at all four inventories, with the largest one being at the second inventory.
No inventory management or scheduling system exists.
Takt time of 314.53 seconds
is less than the total process cycle time (CT/VA) of 351 seconds.
Delivery is either stagnant,
or untimely.
3
2
5
4

## Slide 6: CURRENT & FUTURE CHALLENGES
People
Pandemic (demand) forecasting
Process
Logistics congestion
Technology
Change in engineering and manufacturing standards
Composite and cost-effective materials
Provisional solutions for scalability
Raw materials and intermediate goods scarcity
Quality assurance
Government restrictions and regulations
Talent acquisition,
HR management, and
skills development

## Slide 7: NEXT STEPS
Build and maintain a rapport with public health officials and hospitals.
Maintain and periodically rotate a buffer stock (JIC). Implement the FIFO and Heijunka models (JIT) on the main inventories to avoid pile-ups.
Implement the Kanban scheduling and supermarket management systems.
Be prepared to reliably rent additional equipment, & hire temporary personnel at a moment’s notice.